## Slide 1: E6321 – Adv. Digital Electronics Midterm Project Review
32-bit RISC microprocessor with SIMD extensions design
Team: PlusOneSecond

## Slide 2: Outline
Background
Project Goal
SIMD implementation of Matrix Computations
Block Diagram
Behavioral Description & Verification
Timeline
Reference
Q & A

## Slide 3: Background
Original RISC (SISD):
  Based on loops.
  Fetching of array elements from memory based on individual loads and stores.
  Single Instruction operates on single data (e.g., a scalar).
  Instruction dependences must be identified for each instruction.

## Slide 4: Background
SIMD Architecture:
  SIMD architectures can exploit significant data-level parallelism for:
    Matrix-oriented scientific computing
    Media-oriented image and sound processors
  SIMD is more energy efficient than MIMD
    Only needs to fetch one instruction per data operation
    Makes SIMD attractive for personal mobile devices
  SIMD allows programmer to continue to think sequentially (compared to MIMD) and achieve parallel speedups

## Slide 5: Background
ARM Neon
  Separate sequential and SIMD processors
  Instructions fetched in ARM processor and sent to NEON coprocessor
  Specialized Instructions: VZIP, VMLA, VRSQRTE……
Intel SSE
  SIMD instructions executed along with sequential instructions
  Specialized Instructions: PAVG, DPPS…….

## Slide 6: Project Goal
Execute a full VLSI design flow from RTL design to Place and Route with custom standard cell.
Customize a 32-bit RISC embedded microprocessor with SIMD instruction extensions.
Implement efficient SIMD executions of matrix multiplication, matrix transposition and other computations (e.g. FIR filter).

## Slide 7: SIMD implementation of Matrix Computations
Instruction Set (32-bit instruction word)
  ALU Commands: ADD, SUB, INC…
  Load/store Commands: LD, ST…
  Jump Commands: JMP, JAL, JNC, JC…
  VALU Commands: VADD, VSUB, VAND…
  Transfer Commands: VLD, VST, MOV…
  Shuffle Commands: VSHUF…
  Other: VNOP, VMOL, VMOR…
Shuffle:

## Slide 8: SIMD implementation of Matrix Computations
Matrix Transpose
  Assuming 4*4 matrix:
  Non-SIMD Implementation:
    16 Loads (LD)
    16 Stores (ST)
    Total 32 Instructions
  SIMD Implementation:
    4 Loads (VLD)
    8 Shuffles (VSHUF)
    4 Stores (VST)
    Total 16 Instructions

## Slide 9: SIMD implementation of Matrix Computations
Matrix Multiplication
  Assuming 4*4 matrix:
  Non-SIMD Implementation:
    32 Loads
    For one element:
      4 Multiplications
      3 Adds
    16 Stores
    Total 160 Instructions
  SIMD Implementation:
    8 Loads
    For one row vector:
      4 Multiplications
      8 Shuffles
      3 Adds
    4 Stores
    Total 72 Instructions

## Slide 10: Block Diagram
System
  Memory Interface: control vectorization
  Memory: instructions & Data

## Slide 11: Block Diagram
CPU
  Accumulator-architecture
  Separate Vector Unit

## Slide 12: Block Diagram
Vector Execution Unit
  k * Vector Slice
  Shuffle Unit

## Slide 13: Behavioral Description & Verification
Verified Modules:

## Slide 14: Behavioral Description & Verification

## Slide 15: Timeline
Week 11-12: Behavioral Model, Module Synthesis, Verification
Week 13-14: Overall Synthesis, P&R, Annotation
Week 15-16: Global Design, Timing Closure, Layout

## Slide 16: Reference
Lecture Slides of E6322
Development of a configurable Vector processor, Harald Manske, Fachhochschule Augsbur
OpenCore

## Slide 17: Q & A